## Slide 1: Safe Use of Equipment
Safety Test Series – Exam 2 Review

## Slide 2: Question #1
The actual process of arc welding began in the early _______ when Sir Davey discovered that an electrical current would jump an air gap.
  1870’s

## Slide 3: Question #2
The arc welding _____ is the most important part of the arc welding process.
  machine

## Slide 4: Question #3
The purpose of an arc welding machine is to transform electrical energy into heat energy.
  True – The air gap between the electrode and base metal creates enough heat through resistance for welding to take place.

## Slide 5: Question #4
_______ energy is the type of energy needed for the welding process.
  Heat – Heat is generated through resistance.

## Slide 6: Question #5
Ampere is defined as:
  A unit of measure for the movement of electron flow

## Slide 7: Question #6
Current is defined as:
  The movement of electrons

## Slide 8: Question #7
Resistance is defined as:
  The friction or opposition to electron flow.

## Slide 9: Question #8
Voltage is defined as:
  The force behind the movement of electrons.

## Slide 10: Question #9
Which of the following is not part of an arc welding circuit?
  Electrode holder
  Welding machine
  Welding booth
  Cable lug
    Welding booth

## Slide 11: Question #10
If a welding machine is not properly grounded, the current may enter the welder’s body and cause shock.
  True – It is important to have sufficient ground while welding.

## Slide 12: Question #11
The purpose of the insulation around the jaws of an electrode holder is to prevent the metal jaws from coming in contact with the welding table or the work piece.
  True – Without this insulation, the electrode holder could arc on the base metal.

## Slide 13: Question #12
If the electrode holder being used becomes hot, the cause may be:
  A loose cable clamp or lead or the need for a larger electrode.

## Slide 14: Question #13
Welding cables are made of thousands of hair-like copper wires.
  True

## Slide 15: Question #14
You can assume that a welding machine is safe to use unless it has been disconnected from the outlet and a lock has been placed on the circuit box switch.
  False – Never assume anything.

## Slide 16: Question #15
The purpose of the ground clamp is to provide a path for current to flow from ground cable to the welding machine.
  True – When dealing with electricity, the circuit must be closed in order for welding to occur.

## Slide 17: Question #16
If you find that a ground or electrode cable is loose where it is connected to the ground or electrode lug, you should
  Report it to your instructor

## Slide 18: Question #17
When the electrode holder is forced against the base metal, enough heat energy is produced to cause the electrode and the base metal to melt.
  True – SMAW (stick) and GMAW (mig) use consumable electrodes.

## Slide 19: Question #18
Always check the cable connections to the ground clamp and electrode holder before you start to weld.
  True – Inspection of equipment prior to use is a good practice.

## Slide 20: Question #19
The purpose of wrapping paper or other material around the cable scooper wires is to prevent moisture from gathering on these wires.
  True – Welding cables are wrapped in a material to prevent moisture from gathering on the copper wires.

## Slide 21: Question #20
If you notice a damaged ground or electrode cable, continue to use the welding machine until the instructor tells you that the cables are unsafe.
  False – Never use damaged equipment. An out of order sign should be placed on damaged equipment.