## Slide 1: Operator and Fire Safety
Safety Test Series – Exam 3 Review

## Slide 2: Questions 1
Even thought most metals produce smoke and fumes when being welded, the welder should not be concerned because smoke and fumes only smell bad, they don't harm the eyes or lungs.
  False – Smoke and fumes are very hazardous to human health.

## Slide 3: Question 2
Before a welder cuts or welds a container or tank, the prior liquid contents of the container or tank must be identified.
  True – It is important to identify the prior content and its flammability or combustibility.

## Slide 4: Question 3
"Venting" a container means cutting a hole in the container so the smoke and fumes can escape when the container is being welded.
  False – Prior contents should be identified, container should be cleaned and filled with water. Venting will allow steam or air pressure to be released.

## Slide 5: Question 4
The only reason to put water in a container before welding or cutting the container is to prevent the build-up of heat.
  False – Other reasons include preventing residue from combusting.

## Slide 6: Question 5
No one, including the instructor, should weld on a container unless the prior contents have been determined and the container has been cleaned with the proper cleaners and equipment.
  True

## Slide 7: Question 6
If you are welding and the ventilation system is not working, you should open the doors and windows to produce a draft, or breeze, in the welding area.
  False – A draft or breeze increase the chance of an unwanted fire.

## Slide 8: Question 7
When welding with certain rods on particular types of metals, you should wear a respirator to protect your lungs from the noxious smoke and fumes.
  True – When welding or cutting on galvanized materials, zinc poisoning can occur.

## Slide 9: Question 8
The purpose of a "fire watcher" in a welding area is to watch fires and warn other welders if a fire is becoming too large and dangerous.
  False – The purpose of a fire watcher is to inform the welder of any fire.

## Slide 10: Question 9
A fire blanket is used to put out fires, not to keep finished welding work from cooling off too quickly and cracking.
  True - Fire blankets are to be used to extinguish fires.

## Slide 11: Question 10
The type "A" fire extinguisher is used to extinguish ______ fires.
  Combustible materials such as paper, cloth and wood.

## Slide 12: Question 11
The type "B" fire extinguisher is used to extinguish ______ fires.
  Flammable liquids such as burning oil, gas and paint thinner.

## Slide 13: Question 12
The type "C" fire extinguisher is used to extinguish ______ fires.
  Electrical such as electrical motors, equipment and break boxes.

## Slide 14: Question 13
The type "D" fire extinguisher is used to extinguish _____ fires.
  Combustible metals such as burning zinc, magnesium and titanium.

## Slide 15: Question 14
All welders should practice using a fire extinguisher before a fire breaks out.
  True – Under the supervision of the instructor.

## Slide 16: Question 15
Never stand in water or on a wet surface when welding.
  True – Standing in water increases the chance of electrical shock.

## Slide 17: Question 16
Most fire extinguishers used in the welding area are combination extinguishers, which means that they must be used with other fire extinguishers in order to put out a fire.
  False – Combination extinguishers are used to put out a combination of fire types.

## Slide 18: Question 17
It is permissible to talk to other welders when they are cleaning a weld or using some other equipment in the welding area.
  False – Any type of distraction could cause an accident.

## Slide 19: Question 18
What procedure should be followed before using a grinder?
  Check the grinding wheel for chips and cracks.
  Check the power cord for any defects.

## Slide 20: Question 19
The most serious injury that can be caused by water on the floor, or around the welding cables, is slipping and falling down.
  False – Electrical shock can occur when water is present.

## Slide 21: Question 20
Before starting to weld in any welding area, a welder should know the type and location of every fire extinguisher in the welding area.
  True – A welder should also know the location of the eye wash station and first aid kit.