## Slide 1: Cylinder Safety
Safety Test Series – Exam 4 Review

## Slide 2: Question 1
Cylinders are normally constructed of mild steel plate and can be dented in not handled properly:
  False
  Cylinders are normally constructed of steel and wrought iron as well as rolled, forged, or cast steel.

## Slide 3: Question 2
Until they are given permission by their instructor, welders should not attempt to move cylinders from the storage area:
  True
  It is a good safety practice to seek permission from the instructor before any repairs or refills are made. The instructor is essential the shop manager and management approval is generally required.

## Slide 4: Question 3
Oxygen and acetylene cylinders can be stored together outside the welding area:
  False
  Oxygen and acetylene cylinders stored together create an explosive scenario in the event of a fire. Acetylene and oxygen are two parts of the fire triangle.

## Slide 5: Question 4
If oxygen and acetylene cylinders are stored separately, they must be separated by a 5 foot high wall with a 30 minute burning rating or be separated by at least 20 feet.
  True
  The purpose of the distance or wall is to keep the heat of a small fire from causing the oxygen cylinder safety valve to release.

## Slide 6: Question 5
Both oxygen and acetylene cylinders should be stored vertically.
  True
  All cylinders should be stored vertically and have protective safety caps attached.

## Slide 7: Question 6
If for some reason, an acetylene cylinder has been lying on its side, place it in an upright position and wait at least 15 minutes before using the cylinder.
  True
  The cylinder is filled with a porous material, and then acetone is added to the cylinder, where it absorbs about 24 times its own weight in acetylene. Placing the cylinder upright allows the acetone to even out.

## Slide 8: Question 7
Never move a cylinder that has an attached regulator.
  True
  The exception is if the cylinder is secured by chain to a cylinder cart in use.

## Slide 9: Question 8
Never move a cylinder by rolling it on its edge. It may break the floor or roll over another welder’s foot.
  False
  Rolling cylinders on their edge is the safest way to move a cylinder from place to place in the shop.

## Slide 10: Question 9
If the cylinder does not have a safety cap, the cylinder can be moved if extra safety practices are followed.
  False
  Cylinders should not be handled without the safety cap attached. Cylinder valves could be severely damaged in the event of a fall.

## Slide 11: Question 10
“Cracking” a cylinder means tapping the cylinder valve with a hammer to remove ice, dirt, or water from the valve outlet.
  False
  “Cracking” is a term used to describe opening cylinder valves to blow out any dirt or debris resting in the valves.

## Slide 12: Question 11
The oxygen regulator and hose connections have:
  Right-hand threads
  Oxygen fittings are always right handed and fuel fitting are left handed to insure minimal confusion in assembly.

## Slide 13: Question 12
The acetylene regulator and hose connections have:
  Left-hand threads
  Fuel connections also have a grove in the connecting fitting to indicate a distinguishable difference from oxygen fittings.

## Slide 14: Question 13
Right-hand threads run:
  Clockwise

## Slide 15: Question 14
Left-hand threads run:
  Counterclockwise

## Slide 16: Question 15
Green hoses are used for:
  Oxygen
  Most oxy-fuel hoses today are molded together as one piece and are referred to as a Siamese hose.

## Slide 17: Question 16
The term “purging” means to use oxygen or acetylene gas to clean out dirt and other foreign material from the regulators, hoses, and torch.
  True
  Generally, lines are purged during set-up before cutting or welding begins.

## Slide 18: Question 17
The purpose of the “reverse flow” valve is to prevent oxygen from entering the acetylene hose and acetylene from entering the oxygen hose.
  True
  If the gases being used are allowed to mix in the hose or regulator, they might explode.

## Slide 19: Question 18
The oxygen fittings have a groove around the middle of the connection.
  False
  Fuel fittings have a groove around the middle of the connection.

## Slide 20: Question 19
Cylinders should never be lifted by the valve of safety cap.
  True
  The valve can easily break off or be damaged.

## Slide 21: Question 20
Inert gas cylinders may be stored with oxygen cylinders.
  True
  Inert gases do not react chemically with other substances. Most inert gases used in shops are argon, carbon dioxide, and helium.